## Slide 1
SW Detailed Design
GPT Complementary PWM Modes 1, 2, 3, 4
FPB-RA2T1 | RA2T1 Manual Sec 20.3.3.7 / 20.3.3.8 | Renesas FSP / e2studio
transinh0707-debug | github.com/transinh0707-debug/develop

## Slide 2
What is Complementary PWM?
Three-phase PWM waveform generation with hardware dead time using 3 consecutive GPT16 channels.
Master (ch n)
Triangle wave counter
GTPR cycle, GTDVU dead time
Slave 1 (ch n+1)
Master + GTDVU offset
Neg-phase compare match
Slave 2 (ch n+2)
Linearity counter
0%/100% duty accuracy
Four Operating Modes
0xC
Mode 1
Buffer transfer at crest
0xD
Mode 2
Buffer transfer at trough
0xE
Mode 3
Transfer at crest and trough
0xF
Mode 4
Immediate transfer (bypass chain)

## Slide 3
Modes 1, 2, 3 — Initialization Flow (1/2)
Per RA2T1 Manual Table 20.35 — Steps 1 through 6
1
Set Operating Mode (GTCR.MD)
0xC=Mode1 | 0xD=Mode2 | 0xE=Mode3
Master channel only — slaves follow
2
Select Count Clock (GTCR.TPCS)
Timer prescaler select
Master channel — sets PWM frequency
3
Set Cycle (GTPR, GTPBR, GTPDBR)
Triangle wave period on master channel
Slaves share the cycle register value
4
Set Pin Function (GTIOR.GTIOA/B)
All 3 channels: master + slave1 + slave2
Positive-phase (GTIOCnA) + Negative-phase (GTIOCnB)
5
Enable GTCPPOn Output (GTIOR.PSYE)
Master channel only
PWM synchronous output enable
6
Enable Pin Output (GTIOR.OAE/OBE)
All 3 channels: enable GTIOCnA + GTIOCnB
Positive and negative phase outputs

## Slide 4
Modes 1, 2, 3 — Initialization Flow (2/2)
Per RA2T1 Manual Table 20.35 — Steps 7 through 12
7
Set Buffer Op (GTBER2.CP3DB)
Mode 3 ONLY: enable double buffer
Skip for Mode 1 and Mode 2
8
Set Compare Match (GTCCRA)
All 3 channels: initial duty cycle point
Determines pos/neg phase transition
9
Set Buffer Value (GTCCRD/GTCCRF)
Single buf: GTCCRD only
Double buf (Mode 3): GTCCRD + GTCCRF
10
Set Dead Time (GTDVU)
Master channel only — non-overlap guard
Do NOT use buffer op for GTDVU
11
Start Count (GTCR.CST = 1)
Master channel only — slaves auto-follow
Begins from initial output section
12
Runtime: Update GTCCRD
Write ch0 → ch1 → ch2 GTCCRD (ch2 LAST!)
ch2 triggers temp register transfer

## Slide 5
Mode 4 — Immediate Transfer Design
Per RA2T1 Manual Section 20.3.3.8, Table 20.40 | GTCR.MD = 0xF
Normal Buffer Chain (Modes 1-3)
GTCCRD
Temp A
GTCCRC
GTCCRA
Mode 4 IMMEDIATE bypass: GTCCRD >>> GTCCRA (skips Temp A and GTCCRC)
Double Buffer Path (GTBER2.CP3DB = 1)
GTCCRF
Temp B
GTCCRE
GTCCRA
Mode 4 IMMEDIATE bypass: GTCCRF >>> GTCCRA (skips Temp B and GTCCRE)
CRITICAL: Slave ch2 GTCCRD must be written LAST — triggers simultaneous temp register transfer across all 3 channels

## Slide 6
Counter Operation Sections
Per RA2T1 Manual Tables 20.30 and 20.31
Initial
Output
Master: 0 to DT
After count start
Up-Count
Middle
Master: DT+1
to GTPR-DT
Crest
Section
Master: GTPR-DT+1
to GTPR (up+down)
Down-Count
Middle
Master: GTPR-DT-1
to DT
Trough
Section
Master: DT-1
to 0 (down+up)
Three Counters Working Together
GPT16n.GTCNT (Master)
Triangle wave: 0 to GTPR
Drives the PWM cycle and defines section boundaries
GPT16n+1.GTCNT (Slave 1)
Master counter + GTDVU offset
Range: GTDVU to GTPR+GTDVU | Negative-phase compare
GPT16n+2.GTCNT (Slave 2)
Linearity triangle wave — active only in crest/trough
Ensures accurate duty at 0% and 100% boundaries

## Slide 7
Compare Match & Dead Time Operation
Per RA2T1 Manual Table 20.34 — Waveform Generation Logic
Middle Sections (Up & Down)
Positive ON: GPT16n.GTCNT vs GTCCRA
Negative OFF: GPT16n+1.GTCNT vs GTCCRA
Positive OFF: GPT16n+2.GTCNT vs GTCCRC
Negative ON: GPT16n+1.GTCNT vs GTCCRC
Crest & Trough Sections
Uses GPT16n+2.GTCNT (slave 2)
with GTCCRC / GTCCRE registers
for compare match operations
Ensures linearity at duty 0% and 100%
OFF priority in trough, ON priority in crest
Dead Time Guard (GTDVU Register)
Purpose: Non-overlapping guard between positive and negative phase outputs
Prevents: Shoot-through in H-bridge / half-bridge motor driver circuits
Sequence: Positive OFF > dead time delay > Negative ON (and vice versa)
Sections: Trough = master GTCNT ≤ GTDVU | Crest = slave1 GTCNT > GTPR
WARNING: Do NOT use buffer operation for GTDVU in complementary PWM mode

## Slide 8
Duty Cycle & Key Constraints
Duty Cycle to Compare Match Conversion
GTCCRA ≥ GTPR
Duty = 0%
Positive OFF, Negative ON
GTCCRA = 0
Duty = 100%
Positive ON, Negative OFF
counts = GTPR - (duty_percent × GTPR / 100)
Key Implementation Constraints
Constraint | Requirement
Channels | Must be 3 consecutive GPT16 channels (ch0, ch1, ch2)
GTDVU | 0 < GTDVU < GTPR ¦ No buffer operation allowed
GTCCRD Write Order | ch0 first, ch1 second, ch2 LAST (triggers transfer)
Mode 3 Double Buf | Set GTBER2.CP3DB = 1 on all 3 channels
Mode 4 Immediate | Only guaranteed in up/down-counting middle sections
Start/Stop | Only master channel GTCR.CST controls all 3 channels

## Slide 9
Summary
01
4 complementary PWM modes implemented (crest, trough, both, immediate)
02
3-phase output with hardware dead time for motor control
03
12-step initialization sequence per RA2T1 User's Manual
04
Interactive RTT submenu for runtime configuration
05
Proper buffer chain with slave ch2 LAST write rule
Repository: github.com/transinh0707-debug/develop | Board: FPB-RA2T1 | FSP + e2studio